CPU processor : Intel(R) Core(TM) i5-3570 CPU
Ivy Bridge microarchitecture
Frequency @ 3.40 GHz
3 levels of cache –
L1 = 256 KiB
L2 = 1 MiB
L3 = 6 MiB

System memory = 8GiB DDR3 Synchronous 1600 MHz
Data transfer rate = memory clock rate * bus clock multiplier * data rate * DDR3 module width
= 1600 * 4 * 2 * 8 = 102400 MB/sec

Internal frequency of microprocessors is usually based on Front Side Bus frequency. To calculate internal frequency the CPU multiplies bus frequency by certain number, which is called clock multiplier. It's important to note that for calculation the CPU uses actual bus frequency, and not effective bus frequency. To determine actual actual bus frequency for processors that use dual-data rate buses (AMD Athlon and Duron) and quad-data rate buses (all Intel microprocessors starting from Pentium 4) the effective bus speed should be divided by 2 for AMD or 4 for Intel.

Intel® Core™ i5-3570 Processor	End of Life	Q2'12	4	3.80 GHz	3.40 GHz	6 MB SmartCache	Intel® HD Graphics 2500	$213.00

http://www.cpu-world.com/CPUs/Core_i5/Intel-Core%20i5-3570.html

http://www.icl.utk.edu/~luszczek/teaching/courses/fall2013/cosc530/CS530Project_intel.pdf

L1 cache = 32*3400*10^6 =	108800000000 = 108800 MB/sec
L2 cache = 108800
L3 cache = 108800